## Slide 1: ESAPI Design Patterns
Mike Boberski
Booz Allen Hamilton
boberski_michael@bah.com
(703) 377-0456
November 2009

## Slide 2: Agenda
This presentation explores three common OWASP Enterprise Security API (ESAPI) design patterns. It is intended to be language-independent, i.e., the patterns described in this document are applicable to all language versions of ESAPI. OWASP ESAPI Toolkits are designed to ensure that strong simple security controls are available to every developer in every environment.

## Slide 3: About ESAPI
OWASP ESAPI Toolkits are designed to ensure that strong simple security controls are available to every developer in every environment. All OWASP ESAPI versions are called in the same basic way, as depicted in the figure below.
Notes: Allowing for language-specific differences, all OWASP ESAPI versions have the same basic design:
There is a set of security control interfaces. There is no application logic contained in these interfaces. They define for example types of parameters that are passed to types of security controls. There is no proprietary information or logic contained in these interfaces.
There is a reference implementation for each security control. There is application logic contained in these classes, i.e. contained in these interface implementations. However, the logic is not organization-specific and the logic is not application-specific. There is no proprietary information or logic contained in these reference implementation classes. An example: string-based input validation.
There are optionally your own implementations for each security control. There may be application logic contained in these classes which may be developed by or for your organization. The logic may be organization-specific and/or application-specific. There may be proprietary information or logic contained in these classes which may be developed by or for your organization. An example: enterprise authentication.
There are three common ways to write your own implementations for each security control: using a “built-in” singleton pattern, using an “extended” singleton pattern, or using an “extended” factory pattern. The remainder of this document explores these three design patterns, including situations where taking more than one approach may be appropriate.

## Slide 4: The Built-In Singleton Pattern
The “built-in” singleton pattern refers to the replacement of security control reference implementations with your own implementations. ESAPI interfaces are otherwise left intact.
Notes: The ESAPI security control interfaces include an “ESAPI” class that is commonly referred to as a “locator” class. The ESAPI locator class is called in order to retrieve singleton instances of individual security controls, which are then called in order to perform security checks (such as performing an access control check) or that result in security effects (such as generating an audit record).
Pros of taking this approach include loose coupling between ESAPI and your own implementations.
Cons include the need for developers to understand how to call ESAPI functions with the parameters required by your organization and/or application.

## Slide 5: The Extended Singleton Pattern
The “extended” singleton pattern refers to the replacement of security control reference implementations with your own implementations and the addition/modification/subtraction of corresponding security control interfaces.
Notes: While ESAPI security control reference implementations may perform the security checks and result in the security effects required by your organization and/or application, there may be a need to minimize the need for developers to understand how to call ESAPI functions with the parameters required by your organization and/or application. Availability of training may be an issue, for example. Another example would be to facilitate enforcing a coding standard.
Pros of taking this approach are the lessening of the need for developers to understand how to call ESAPI functions with the specific parameters required by your organization and/or application. Pros also include minimizing or eliminating the ability for developers to call ESAPI functions that deviate from your organization’s and/or application’s policies.
Cons result from the tight coupling between ESAPI and your own implementations: you will need to maintain both the modified security control reference implementations and the modified security control interfaces (as new versions of ESAPI are released over time).

## Slide 6: The Extended Factory Pattern
The “extended” factory patterns refers to the addition of a new security control interface and corresponding implementation, which in turn calls ESAPI security control reference implementations and/or security control reference implementations that were replaced with your own implementations. The ESAPI locator class would be called in order to retrieve a singleton instance of your new security control, which in turn would call ESAPI security control reference implementations and/or security control reference implementations that were replaced with your own implementations.

## Slide 7: Where to Go From Here
OWASP is the premier site for Web application security. The OWASP site hosts many projects, forums, blogs, presentations, tools, and papers. Additionally, OWASP hosts two major Web application security conferences per year, and has over 80 local chapters. The OWASP ESAPI project page can be found here http://www.owasp.org/index.php/ESAPI
The following OWASP projects are most likely to be useful to users/adopters of ESAPI:
  OWASP Application Security Verification Standard (ASVS) Project - http://www.owasp.org/index.php/ASVS
  OWASP Top Ten Project - http://www.owasp.org/index.php/Top_10
  OWASP Code Review Guide - http://www.owasp.org/index.php/Category:OWASP_Code_Review_Project
  OWASP Testing Guide - http://www.owasp.org/index.php/Testing_Guide
  OWASP Legal Project - http://www.owasp.org/index.php/Category:OWASP_Legal_Project
Similarly, the following Web sites are most likely to be useful to users/adopters of ESAPI:
  OWASP - http://www.owasp.org
  MITRE - Common Weakness Enumeration – Vulnerability Trends, http://cwe.mitre.org/documents/vuln-trends.html
  PCI Security Standards Council - publishers of the PCI standards, relevant to all organizations processing or holding credit card data, https://www.pcisecuritystandards.org
  PCI Data Security Standard (DSS) v1.1 - https://www.pcisecuritystandards.org/pdfs/pci_dss_v1-1.pdf

## Slide 8: Questions?

## Slide 9: Additional Slide – Design Patterns Book
Includes code snippets for this presentation
http://www.owasp.org/images/8/82/Esapi-design-patterns.pdf